## Slide 1: GESTÃO DE REDES / NETWORK MANAGEMENT Notas complementares / Complementary notes
NETCONF + YANG RESTCONF

## Slide 2: Introduction
Networks Operators complained that configuration management was not being addressed by IETF! (RFC3535)
But, can’t we do it with existing management technology? Do we need a new one?
SNMP / SMIv2 / MIBs
COPS-PR /SPPI /PIBs
CLI / TELNET / SSH
SIM / MOP / UML / PCIM
HTTP / HTML
XML

## Slide 3: Introduction
  What about SNMP?
Works very well for device monitoring
The stateless nature of SNMP is useful for statistical and status polling.
Core MIBs implemented everywhere!
Many proprietary MIBs available & supported
Important for event correlation, alarm detection, and root cause analysis
Too little deployment of writable MIB modules! (devices are not fully configurable by SNMP)
The transactional model and the protocol constraints make it more complex to implement MIBs
Scaling problems with regard to the number of objects in a device
Semantic mismatch between the task-oriented view and data-centric view (no high level proc.)
SNMP / SMI / MIBs
Standard MIB modules often lack writable MIB objects which can be used for configuration
SNMP requires applications to be useful: Designed as a programmatic interface between management applications and devices.

## Slide 4: Introduction
  What about CLI / TELNET / SSH ?
A saved sequence of textual commands can easily be replayed
It is natural to use the same interface users already use and same abstractions for automating configuration change
Command line interface (CLI) does not require any special purpose applications
CLI are task-oriented by nature…
Most command line interfaces provide context sensitive help (reduced learning curve)
Some CLI interfaces lack a common data model (different behavior between vendors)
Command line interface is primarily targeted to humans (who can adjust to changes easily)
CLI lack of proper version control for the syntax and the semantic (difficult to maintain)
Not efficient in multi-vendor environments
Access control is often ad-hoc and insufficient
CLI / TELNET / SSH
It is still a common practice to use TELNET/SSH to access and configure devices using their CLI

## Slide 5: Introduction
  What about HTTP / HTML ?
Embedded web servers for configuration are end-user friendly and solution oriented
Suitable for configuring consumer devices by inexperienced users
No need for specialized applications (only a web browser is required)
Embedded web servers are management application hostile (difficult to use by programs)
Replay of configuration is often problematic (different versions of same device may use different interface)
The access control facilities are often ad-hoc and sometimes insufficient.
HTTP / HTML
Many devices have an embedded web server which can be used to configure the device and to obtain status information. Access and configuration through HTTP/HTML are common.

## Slide 6: Requirements
Network Operators identified Requirements (RFC3535):
  Easy to use (a key requirement!)
  Clear distinction between configuration data, operational state and statistics (which parameters were really administratively configured?)
  To fetch separately configuration data, operational state data, and statistics…
  Enable operators to concentrate on the configuration of the entire network as a whole, rather than individual devices
  Support configuration transactions across a number of devices…
  Operational change from config A to config B with minimal state changes. Minimize the possible impact of config changes.
  Need standards for pulling and pushing configurations from devices
  It must be easy to do consistency checks of configurations over time, per link…
  (…)

## Slide 7: Requirements
(… )
  Network wide configurations are typically stored in central master databases (…) standardize the common parts of these network wide configuration database schemas
  Use text tools, like diff or version control (…) devices should not reorder data
  A role-based access control model and the principle of least privilege…
  To do consistency checks of access control lists across devices
  Distinguish between the distribution of configurations and the activation of a certain configuration. Devices should be able to hold multiple configurations
  it is a requirement to support both data-oriented and task-oriented access control

## Slide 8: NETCONF / YANG
Image from https://medium.com/@k.okasha/network-automation-and-the-rise-of-netconf-e96cc33fe28

## Slide 9: NETCONF / YANG
NETCONF: Network Configuration Protocol
YANG: Yet Another Next Generation
This protocol defines a simple mechanism where network management applications, acting as clients, can invoke operations on the devices, which act as servers.
Configuration data information can be retrieved, and new configuration data can be uploaded and manipulated.
NETCONF specification [RFC4741] defines a small set of operations
Avoid making any requirements on the data carried on those operations  Data Agnostic
YANG is a data modeling language used to model configuration and state data manipulated by NETCONF [RFC6020]
Allowing both standard and proprietary data models to be published (human readable)
YANG allows a modeler to create a data model, to define the organization of the data in that model, and to define constraints on that data.

## Slide 10: NETCONF
Different paradigm:
  task-oriented approach  not data-centric as in SNMP
  Over a connection-oriented transport service (usually SSH)
  Includes mechanisms for controlling configuration datastores
  A NETCONF session is the logical connection between a network administrator or network configuration application and a network device.
  All NETCONF operations are carried out within a session
  The NETCONF server is required to authenticate the entity requesting a session before processing any request
  NETCONF messages MUST be well-formed XML, encoded in UTF-8
XML-based remote procedure call (RPC) mechanism

## Slide 11: NETCONF: XML-based RPC
What is RPC (Remote Procedure Call)?

## Slide 12: NETCONF: Layers
Image from https://www.ietf.org/slides/slides-edu-network-configuration-with-netconf-00.pdf
Notice the colors: they show relation between the layers and the encapsulation of data in PDUs

## Slide 13: NETCONF: Operations
The NETCONF standard (RFC 4741) defined the following operations that can be executed against the different data store
RFC6241 updated with some variants like a confirmed commit and a validate:

## Slide 14: NETCONF: Configuration Databases
There may exist several configuration databases on devices
Not all devices implement them all (not required)
NETCONF operations are targeted to lock – retrieve – edit – save – copy – unlock configs on any of those data stores
Image from https://medium.com/@k.okasha/network-automation-and-the-rise-of-netconf-e96cc33fe28

## Slide 15: NETCONF: Configuration Databases
Only one Configuration:
<RUNNING>
Two Configurations:
<RUNNING>
<STARTUP>
Two Configurations:
<CANDIDATE>
<RUNNING>
All config DBs!
Image from http://www.netconfcentral.org/netconf_docs

## Slide 16: NETCONF: Configuration Databases
New model recently proposed (RFC 8342, March 2018)
<candidate>
(ct, rw)
<running>
(ct, rw)
<startup>
(ct, rw)
<intended>
(ct, ro)
<operational>
(ct + cf, ro)
System State
Subject to validation //
Dynamic Configuration Datastores
Learned configuration
System configuration
System configuration
// config. transformations, e.g. removal of // nodes marked “inactive”, expansion of // templates…

## Slide 17: NETCONF & YANG
The NETCONF client and server are driven by the content of YANG modules
Server (device)
YANG Models
Client (App)
NETCONF Engine
<rpc>
<rpc-reply>
configuration
state data
notifications
operations
metadata
system software component
config database

## Slide 18: YANG version 1.1
YANG is a language originally designed to model data for the NETCONF protocol (RFC 7950, august 2016)
  Standard Modules and Proprietary Models: define configuration data, RPC, notifications
  Defines hierarchies of data that can be used in operations (configuration, state data, etc.)
  Data organized as a tree, where every node has a name and either a value or a set of child nodes;
Modules and Submodules
Top-level
Leaf Node
Leaf-List Nodes
contains simple data, like integer or string
defines a sequence of list entries
Container Nodes
List Nodes
used to group related nodes in a subtree
defines a sequence of values of a type

## Slide 19: YANG version 1.1
example-system model
module example-system {
yang-version 1.1;
namespace "urn:example:system";
prefix "sys";
organization "Example Inc.";
contact "joe@example.com";
description
"The module for entities implementing the Example system.";
revision 2007-06-09 {
description "Initial revision.";
}
………
}
<?xml version="1.0" encoding="UTF-8"?>
<module name="example-system"
xmlns="urn:ietf:params:xml:ns:yang:yin:1"
xmlns:sys="urn:example:system">
<yang-version value="1.1"/>
<namespace uri="urn:example:system"/>
<prefix value="sys"/>
<organization>
<text>Example Inc.</text>
</organization>
<contact>
<text>joe@example.com</text>
</contact>
<description>
<text>The module for entities implementing the Example system.</text>
</description>
<revision date="2007-06-09">
<description>
<text>Initial revision.</text>
</description>
</revision>
…
YANG
XML
$ pyang –f yin example-system.yang

## Slide 20: YANG version 1.1
Leaf Node example
Leaf-List Node example
leaf host-name {
type string;
description
"Hostname for this system.";
}
<host-name>my.example.com</host-name>
YANG
XML
Leaf node has:
  - one value; no children; one instance
leaf-list domain-search {
type string;
description
"List of domain names to search.";
}
<domain-search>high.example.com</domain-search>
<domain-search>low.example.com</domain-search>
<domain-search>every.example.com</domain-search>
YANG
XML
Leaf-List node has:
  - one value; no children; multiple instances;

## Slide 21: YANG version 1.1
Container Node example
container system {
container login {
leaf message {
type string;
description
"Message given at start of login session.";
}
}
<system>
<login>
<message>Good morning</message>
</login>
</system>
YANG
XML
Container node has:
  - no value; only child nodes; any number of child nodes of any type;

## Slide 22: YANG version 1.1
List Node example
list user {
key "name";
leaf name {
type string;
}
leaf full-name {
type string;
}
leaf class {
type string;
}
}
<user>
<name>glocks</name>
<full-name>Goldie Locks</full-name>
<class>intruder</class>
</user>
<user>
<name>snowey</name>
<full-name>Snow White</full-name>
<class>free-loader</class>
</user>
<user>
<name>rzell</name>
<full-name>Rapun Zell</full-name>
<class>tower</class>
</user>
YANG
XML
List node has:
  - each entry is like a container identified by key; defines multiple key leafs; any number of child nodes of any type;

## Slide 23: YANG version 1.1
RPC definition
<rpc message-id="101"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<activate-software-image xmlns="http://example.com/system">
<image-name>example-fw-2.3</image-name>
</activate-software-image>
</rpc>
<rpc-reply message-id="101"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<status xmlns="http://example.com/system">
The image example-fw-2.3 is being installed.
</status>
</rpc-reply>
XML
Example 1:
An RPC operation with one input parameter and one output result
rpc activate-software-image {
input {
leaf image-name {
type string;
}
}
output {
leaf status {
type string;
}
}
}
YANG

## Slide 24: YANG version 1.1
RPC definition
<rpc message-id="102"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<action xmlns="urn:ietf:params:xml:ns:yang:1">
<interface xmlns="http://example.com/system">
<name>eth1</name>
<ping>
<destination>192.0.2.1</destination>
</ping>
</interface>
</action>
</rpc>
<rpc-reply message-id="102"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0"
xmlns:sys="http://example.com/system">
<sys:packet-loss>60</sys:packet-loss>
</rpc-reply>
XML
Example 2:
An RPC operation tied to a list!
list interface {
key "name";
leaf name {
type string;
}
action ping {
input {
leaf destination {
type inet:ip-address;
}
}
output {
leaf packet-loss {
type uint8;
}
}
}
}
YANG

## Slide 25: YANG version 1.1
Notification example
notification link-failure {
description
"A link failure has been detected.";
leaf if-name {
type leafref {
path "/interface/name";
}
}
leaf if-admin-status {
type admin-status;
}
leaf if-oper-status {
type oper-status;
}
}
<notification
xmlns="urn:ietf:params:netconf:capability:notification:1.0">
<eventTime>2007-09-01T10:00:00Z</eventTime>
<link-failure xmlns="urn:example:system">
<if-name>so-1/2/3.0</if-name>
<if-admin-status>up</if-admin-status>
<if-oper-status>down</if-oper-status>
</link-failure>
</notification>
YANG
XML

## Slide 26: NETCONF: Example workflow
  Client: open an SSH connection to port 830 (NETCONF PORT) or to any other port and request NETCONF subsystem
  Client: say “Hello” and provide supported capabilities
  Server: answers with its own supported capabilities
  Client: call remote procedures…
  Client/Server: close the session
Image from https://www.ietf.org/slides/slides-edu-network-configuration-with-netconf-00.pdf

## Slide 27: NETCONF simple example
STEP 1: <hello>
C
S
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.1">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
<capability> urn:ietf:params:netconf:capability:writable-running:1.0 </capability>
<capability>urn:ietf:params:netconf:capability:candidate:1.0 </capability>
</capabilities>
<session-id>5</session-id>
</hello>
<?xml version="1.0" encoding="UTF-8"?>
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.1">
<capabilities>
<capability>urn:ietf:params:netconf:base:1.1</capability>
</capabilities>
</hello>
S
C

## Slide 28: NETCONF simple example
STEP 2: <get> all model data from device
C
S
<rpc-reply message-id="102” xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<data>
<!-- ... entire set of data returned ... -->
</data>
</rpc-reply>
<rpc message-id="102” xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<get/>
</rpc>
S
C

## Slide 29: NETCONF simple example
STEP 3: <get> filter model data from device
C
S
<rpc-reply message-id="103"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<data>
<t:top xmlns:t="http://example.com/schema/1.2/stats">
<t:interfaces>
<t:interface t:ifName="eth0">
<t:ifInOctets>45621</t:ifInOctets>
<t:ifOutOctets>774344</t:ifOutOctets>
</t:interface>
</t:interfaces>
</t:top>
</data>
</rpc-reply>
<rpc message-id="103” xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<get>
<filter type="subtree">
<t:top xmlns:t="http://example.com/schema/1.2/stats">
<t:interfaces>
<t:interface t:ifName="eth0"/>
</t:interfaces>
</t:top>
</filter>
</get>
</rpc>
S
C

## Slide 30: NETCONF simple example
STEP 4: <close-session>
C
S
<rpc-reply message-id="104"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<ok/>
</rpc-reply>
<rpc message-id="104"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<close-session/>
</rpc>
S
C

## Slide 31: NETCONF Advanced example
Example1: configuration update against a single device
  Acquiring the configuration lock.
  Checkpointing the running configuration.
  Loading and validating the incoming configuration.
  Changing the running configuration.
  Testing the new configuration.
  Making the change permanent (if desired).
  Releasing the configuration lock.

## Slide 32: NETCONF Advanced example
Step 1: A lock should be acquired to prevent simultaneous updates from multiple sources
  If :candidate capability is available, the candidate configuration should be locked
<rpc message-id="101"
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<lock>
<target>
<running/>
</target>
</lock>
</rpc>
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<lock>
<target>
<candidate/>
</target>
</lock>
</rpc>

## Slide 33: NETCONF Advanced example
Step 2: The running configuration can be saved into a local file as a checkpoint
  To restore the checkpoint file, reverse the <source> and <target> parameters
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<copy-config>
<target>
<url>file://checkpoint.conf</url>
</target>
<source>
<running/>
</source>
</copy-config>
</rpc>

## Slide 34: NETCONF Advanced example
Step 3 If the :candidate capability is supported, the configuration can be loaded onto the device without impacting the running system
  If the device supports the :validate:1.1 capability, validate it:
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<edit-config>
<target>
<candidate/>
</target>
<config>
<!-- place incoming configuration changes here -->
</config>
</edit-config>
</rpc>
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<validate>
<source>
<candidate/>
</source>
</validate>
</rpc>

## Slide 35: NETCONF Advanced example
Step 4: Changing the Running Configuration
  If the device supports the :candidate, commit the changes to running
  If not, the configuration change is loaded directly into running
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<commit>
<confirmed/>
<confirm-timeout>120</confirm-timeout>
</commit>
</rpc>
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<edit-config>
<target>
<running/>
</target>
<config>
<!-- place incoming configuration changes here -->
</config>
</edit-config>
</rpc>

## Slide 36: NETCONF Advanced example
Step 5: Testing the New Configuration
  To gain confidence, the application can run tests of the operational state of the device.
Step 6: Making the Change Permanent
  If the device supports the :startup capability, make changes permanent
  If device supports :candidate, and a confirmed commit was request, the confirming commit must be send before timeout or it will be reverted! (Why?)
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<copy-config>
<target>
<startup/>
</target>
<source>
<running/>
</source>
</copy-config>
</rpc>
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<commit/>
</rpc>

## Slide 37: NETCONF Advanced example
Step 7: Releasing the Configuration Lock
  If the :candidate capability is supported, the unlock operation is performed on the candidate…
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<unlock>
<target>
<running/>
</target>
</unlock>
</rpc>
<rpc message-id="101”
xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<unlock>
<target>
<candidate/>
</target>
</unlock>
</rpc>

## Slide 38: NETCONF Advanced example
Example 2: Operations on Multiple Devices
  Transaction semantics is required!
  NETCONF protocol contains sufficient primitives upon which transaction-oriented operations can be built
  Complete transactional support among all devices is prohibitively expensive!
  But… we may reduce the size and number of windows for failure scenarios!
  Classes of multidevice operation:
    the operation can fail on individual devices without requiring all devices to revert to their original state!
     Repeat the operation later… on that device only
    the operation should complete on all devices or be fully reversed.
       The same steps used in single-device operations are used, but are performed in parallel across all devices! If any step fails, the previous configurations can be restored!

## Slide 39: RESTCONF
RESTCONF
  RESTCONF uses HTTP methods to implement the equivalent of NETCONF operations, enabling basic CRUD operations on a hierarchy of conceptual resources.
    Create (POST), Read (GET), Update (PUT), Delete (DELETE)
  RESTCONF is not intended to replace NETCONF, but rather to provide an HTTP interface
  The HTTP POST, PUT, PATCH, and DELETE methods are used to edit data resources represented by YANG data model
  RESTCONF does not need to mirror the full functionality of the NETCONF protocol

## Slide 40: RESTCONF
Coexistence with NETCONF
  t is possible that locks are in use on a RESTCONF server, even though RESTCONF cannot manipulate locks. In such a case, the RESTCONF protocol will not be granted write access to data resources within a datastore.
Network Device
Client (App)
RESTCONF
Datastore
Web App
NETCONF

## Slide 41: RESTCONF Example
Retrieve the Top-Level API Resource
GET /.well-known/host-meta HTTP/1.1
Host: example.com
Accept: application/xrd+xml
HTTP/1.1 200 OK
Content-Type: application/xrd+xml
Content-Length: nnn
<XRD xmlns='http://docs.oasis-open.org/ns/xri/xrd-1.0’>
<Link rel='restconf' href='/restconf’/>
</XRD>

## Slide 42: RESTCONF Example
The client may then retrieve the top-level API resource
GET /restconf HTTP/1.1
Host: example.com
Accept: application/yang-data+json
HTTP/1.1 200 OK
Date: Thu, 26 Jan 2017 20:56:30 GMT
Server: example-server
Content-Type: application/yang-data+json
{
"ietf-restconf:restconf" : {
"data" : {},
"operations" : {},
"yang-library-version" : "2016-06-21”
}
}
In JSON or XML…

## Slide 43: RESTCONF Example
Retrieve the Server Capability Information
GET /restconf/data/ietf-restconf-monitoring:restconf-state/capabilities HTTP/1.1
Host: example.com
Accept: application/yang-data+xml
HTTP/1.1 200 OK
Date: Thu, 26 Jan 2017 20:56:30 GMT
Server: example-server
Cache-Control: no-cache
Last-Modified: Thu, 26 Jan 2017 16:00:14 GMT
Content-Type: application/yang-data+xml
<capabilities xmlns="urn:ietf:params:xml:ns:yang:ietf-restconf-monitoring">
<capability>\
urn:ietf:params:restconf:capability:defaults:1.0?\
basic-mode=explicit\
</capability>
….
</capabilities>

## Slide 44: References
http://www.netconfcentral.org/
https://ripe68.ripe.net/presentations/181-NETCONF-YANG-tutorial-43.pdf
https://datatracker.ietf.org/wg/netconf/documents/
https://www.cisco.com/c/en/us/support/docs/storage-networking/management/200933-YANG-NETCONF-Configuration-Validation.html
http://www.yumaworks.com/support/download-yumapro-client/
https://tools.ietf.org/html/rfc3535
https://tools.ietf.org/html/rfc6241
https://tools.ietf.org/html/rfc6020
https://tools.ietf.org/html/rfc6244
https://tools.ietf.org/html/rfc8040
https://www.ietf.org/slides/slides-edu-network-configuration-with-netconf-00.pdf
https://medium.com/@k.okasha/network-automation-and-the-rise-of-netconf-e96cc33fe28